## Slide 1: ALGORITHMS IN HARDWARE
Abstract
The application of cryptographic algorithms in hardware is utilized for security and performance reasons in various public-key cryptosystems. The overall aim of the project is to implement algorithms in hardware. The design of the algorithm and logic circuit for a systolic system for modular exponentiation has been defined by Kornerup in A Systolic, Linear-Array Multiplier for a Class of Right-Shift Algorithms [1]. In order to design this algorithm in VHDL, some other functions were first developed.
Simon Karing • Mathias Helsengren • Mads Riis Rasmussen • Kim Hoang Le
The Project
The goal of this project is to present one such algorithm, a systolic modular exponentiation system, in VHDL on our FPGA board.
Conclusion
We encountered a wide degree of problems throughout our project. This included both software and hardware problems, some of which we were able to overcome. Despite our best efforts at fixing a copying mechanism on the modular exponentiator, and after numerous hours and a great deal of testing, the systolic system for modular exponentiation was not a working construction.
Method
In order to reach the projects goal, we familiarized ourselves with the hardware programming language VHDL, its function on the FPGA board, and Montgomery’s Residue (M-res) for modular arithmetic. Modular exponentiation uses M-res to allow hardware to work in parallel and optimize speed.
Systolic Multiplier Cell
The systolic multiplier cell can be connected in a series to multiply larger numbers. The numbers are taken in binary and is also output in binary through a shift register.
Full Adder
The full adder takes 3 inputs and gives 2 outputs