## Slide 1: THE CYCLE OF BITS
Abstract
The application of cryptographic algorithms in hardware is utilized for security and performance reasons in various public-key cryptosystems. In order to design a modular exponentiator, the modular multiplier must first be created in accordance with Kornerup’s definitions in A Systolic, Linear-Array Multiplier for a Class of Right-Shift Algorithms. In order to design these algorithms in VHDL, some other basic functions were first developed. We were unable to design a working construction of the modular exponentiator but we were able to design a working modular multiplier.
Simon Karing • Mathias Helsengren • Mads Riis Rasmussen • Kim Hoang Le
The Project
The purpose of this project was to implement algorithms in hardware and focused towards working with something usable in cryptography, the modular exponentiator ( ).
Conclusion
We encountered a wide degree of problems throughout our project. This included both software and hardware problems, some of which we were able to overcome. Through numerous tests of correct and incorrect inputs, we can conclude that we were able to create a modular multiplier, and it works as it is intended.
Method
In order to reach the projects goal, we familiarized ourselves with the hardware programming language VHDL, its function on the FPGA board, and Montgomery’s Residue for modular arithmetic. VHDL stands for Very High Speed Integrated Circuit Hardware Description Language and FPGA stands for field-programmable gate arrays.
Modular exponentiation uses Montgomery’s residue to allow hardware to work in parallel and optimize speed. To design a modular multiplier and exponentiator, the creation of other basic functions for logic design were first developed. These functions include flip flops, shift registers, and a full adder.
Systolic Modular Multiplier Cell
The systolic modular multiplier cell can be connected in a series to multiply larger numbers. The numbers are taken in binary and is also output in binary through a shift register. The binary number inputs and outputs are in Montgomery’s residue. This residue is calculated as follows: where , , and .
The output goes to in the first cycles and then goes to the result shift register for the next cycles.
Full Adder
The full adder takes 3 inputs and gives 2 outputs. The full adder then outputs to oaccording to how many of the 3 inputs which is set to 1.
Group 65b
Algorithm MM
IMADA 2017
Shift Register
The shift register is a series of flip flops (bit information storage units) that takes an input, and waits until the clocks rising edge to change the value of the flip flop. Its purpose is to store information which can only be manipulated during a rising edge, and in our case, it is an array of bits representing inputs and outputs.