## Slide 1: ALGORITHMS IN HARDWARE
Abstract
The application of cryptographic algorithms in hardware is utilized for security and performance reasons in various public-key cryptosystems. The overall aim of the project is to implement algorithms in hardware. The design of the algorithm and logic circuit for a systolic system for modular multiplication and exponentiation has been defined by Kornerup in A Systolic, Linear-Array Multiplier for a Class of Right-Shift Algorithms. In order to design these algorithms in VHDL, some other functions were first developed.
Simon Karing • Mathias Helsengren • Mads Riis Rasmussen • Kim Hoang Le
The Project
We managed to implement a working systolic modular multiplier in VHDL on our FPGA board.
Conclusion
We encountered a wide degree of problems throughout our project. This included both software and hardware problems, some of which we were able to overcome. Despite our best efforts at fixing a copying mechanism on the modular exponentiator, and after numerous hours and a great deal of testing, the systolic system for modular exponentiation was not a working construction.
Method
In order to reach the projects goal, we familiarized ourselves with the hardware programming language VHDL, its function on the FPGA board, and Montgomery’s Residue (M-res) for modular arithmetic. VHDL stands for Very High Speed Integrated Circuit Hardware Description Language and FPGA stands for field-programmable gate arrays.
Modular exponentiation uses M-res to allow hardware to work in parallel and optimize speed. To design a modular multiplier or exponentiator, the creation of other basic functions for logic design were first developed. These functions include flip flops, shift registers, and a full adder.
Systolic Modular Multiplier Cell
The systolic modular multiplier cell can be connected in a series to multiply larger numbers. The numbers are taken in binary and is also output in binary through a shift register. The binary number inputs and outputs are in Montgomery’s residue. This residue is calculated as follows: where and .
The output goes to in the first cycles and then goes to the result shift register for the next cycles.
Full Adder
The full adder takes 3 inputs and gives 2 outputs
Group 65b
Algorithm MM
Shift Register
The shift register is a series of flip flops that takes an input during the rising edge of a clock cycle.